## Slide 1: Characterization of C2MOS Flip-Flop in Sub-Threshold Region
Baile Chen, Keye Sun

## Slide 2: Outline
Motivation
Energy & Delay Comparison of 4 types of Flip-Flops
Timing characterization of C2MOS
Vdd & Size Effects
Conclusion
References

## Slide 3: Motivation
Sub-threshold circuits are one of the solution to the ultra-low energy systems while Flip-Flops are essential timing blocks in digital circuits.
tsu, thold, tc-q are affected by process variation.
Timing & energy characterization of sub-threshold Flip-Flops should be done to get the correct design of Flip-Flops.

## Slide 4: Motivation
C2MOS FF is one of the promising FFs in sub-threshold circuits.
Prevent CLK overlap
Eliminate ratio problem
Stack effect to reduce Ioff , thus increasing Ion/Ioff

## Slide 5: Energy & Delay Comparison of 4 types of FFs
TGFF C2MOS
HLFF SDFF

## Slide 6: Comparison Results
Low power consumption compared
with SDFF and HLFF
Power consumption is almost the
same as TGFF but C2MOS can
release the clock overlap problem
while TGFF cannot.
C2MOS has lower clk-to-Q delay.
Chart: Clk-to-Q Delay Comparison of 4 types of FFs
| TGFF | C2MOS | SDFF | HLFF
0-1 transition | 5.429 | 5.4771 | 10.9669 | 11.1684
1-0 transition | 7.33 | 4.1869 | 16.3779 | 7.378
Chart: Comparison of Energy Consumption of 0-0,0-1,1-0,1-1 Transitons for 4 Types of FFs
| TGFF | C2MOS | SDFF | HLFF
0-0 | 49.181 | 98.9909 | 527.074 | 432.06
0-1 | 124.135 | 160.201 | 447.091 | 1014.72
1-0 | 148.222 | 172.912 | 870.742 | 649.964
1-1 | 44.8918 | 104.173 | 201.4 | 777.116

## Slide 7: Timing Characterization
The setup time of the Flip-Flop has a lognormal pattern due to the output of the combinational logic.
The setup time will result in the failure of functionality. It should be noted that the setup and hold time should be in the safe operation region to ensure the correct functionality.
Comb.
Logic
delay setup
D Q
clk
delay clk-Q

## Slide 8: Result
Parameters Definition:
tsu: time from D input valid to the triggering edge
thold: time for which the D input is valid after the triggering edge
clk-to-Q delay: time from the triggering edge until valid data is available at Q output
Failure of the functionality due to the metastability of the Flip-Flops
Chart: Dependence Between Setup/Hold Times and Clk-to-Q Delay for C2MOS FF
| 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9000000000000001 | 2 | 3 | 4 | 5 | 10 | 20
Setup time | 15.638 | 12.0078 | 10.0119 | 8.7429 | 7.897 | 7.3503 | 7.0035 | 6.1845 | 6.0204 | 5.968 | 5.8948 | 5.8153
Hold time | 6.5814 | 5.9497 | 5.7 | 5.7248 | 5.8153
D-to Q delay | 17.038 | 13.5078 | 11.6119 | 10.4429 | 9.697 | 9.2503 | 9.0035 | 9.1845 | 10.0204 | 10.968 | 15.8948 | 25.8153
Failure

## Slide 9: Variability of Timing Using Monte-Carlo Simulation
Chart: Failure Probability VS Setup time
| 1.35 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9000000000000001 | 2 | 3 | 4 | 5 | 10
Failure Probability | 0.53 | 0.48 | 0.35 | 0.25 | 0.2 | 0.17 | 0.14 | 0.07 | 0.04 | 0 | 0 | 0
Chart: Clk-to-Q Delay VS Setup Time
| 1.6 | 1.7 | 1.8 | 1.9000000000000001 | 2 | 3 | 4 | 5 | 10
clk-to-Q mean | 11.4246 | 10.0714 | 8.6773 | 7.911 | 7.3639 | 6.2017 | 6.0352 | 5.9956 | 5.8641
D-to-Q delay | 13.0246 | 11.7714 | 10.4773 | 9.811 | 9.3639 | 9.2017 | 10.0352 | 10.9956 | 15.8641
Chart: Standard Deviation VS Setup Time
| 1.6 | 1.7 | 1.8 | 1.9000000000000001 | 2 | 3 | 4 | 5 | 10
C-Q Std.Dev. | 8.2352 | 5.1255 | 8.6773 | 2.7649 | 2.3358 | 1.6531 | 1.5643 | 1.5094 | 1.6145
Optimum D-to-Q
The FF becomes reliability-driven instead of optimum-timing driven in sub-threshold region.

## Slide 10: Turning Knobs - Vdd
Chart: Relation of Energy per Operation and Vdd
| 0.18000000000000019 | 0.2 | 0.30000000000000032 | 0.4 | 0.60000000000000064 | 0.8
Energy [E-16 J] | 1.02 | 1 | 1.55 | 2.95 | 7.19 | 18.8
Chart: Relation of Delay and Vdd
| 0.18000000000000019 | 0.2 | 0.30000000000000032 | 0.4 | 0.60000000000000064 | 0.8
C-Q Delay [ns] | 64.9469 | 40.857 | 5.8395 | 1.6131 | 0.4295 | 0.1501

## Slide 11: Failure Prob. VS Vdd for Different Sizes
65:65 circuits has higher failure probability than 130:130 circuits due to larger effects of process variation on smaller size devices.
Unbalanced PMOS and NMOS circuit shows higher failure probability possibly because of unbalanced effects of variation on weak and strong devices.
Chart: Failure Prob. VS Vdd
| 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001 | 0.15 | 0.16 | 0.17 | 0.18
Wp:Wn=65:65 | 0.99 | 0.97 | 0.95 | 0.88 | 0.76 | 0.52 | 0.1 | 0 | 0
Wp:Wn=130:65 | 0.98 | 0.92 | 0.72 | 0.34 | 0.12 | 0.01 | 0
Wp:Wn=130:130 | 0.99 | 0.94 | 0.83 | 0.5 | 0.27 | 0.04 | 0 | 0

## Slide 12: Turning Knobs - Size
Chart: Energy Consumption for 0-1 Transition VS Width
| 65 | 75 | 80 | 95 | 110 | 150 | 200
Energy [E-16J] | 1.9158 | 1.9519 | 2.0106 | 2.1048 | 2.2 | 2.457 | 2.7701
Chart: Clk-to-Q Delay VS Width
| 65 | 75 | 80 | 95 | 110 | 150 | 200
Delay [ns] | 3.597 | 3.4337 | 3.1282 | 2.8336 | 2.6271 | 2.3828 | 2.3915

## Slide 13: Energy – Delay Relationship
Size has smaller effect compared with Vdd effect since the former has only linear effect while the latter has exponential effect.
Chart: Clk-to-Q Delay VS Energy Consumption for 0-1 Transition
| 1.9157999999999988 | 1.9519 | 2.0105999999999997 | 2.1048 | 2.2000000000000002 | 2.4569999999999976
Size Effect | 3.597 | 3.4337 | 3.1282 | 2.8336 | 2.6271 | 2.3828
Vdd Effect | 64.9469 | 40.857 | 5.8395 | 1.6131 | 0.4295 | 0.1501

## Slide 14: Conclusion
A timing model for FF operating at sub-threshold voltages has been used to characterize C2MOS Flip-Flop.
It has been shown that optimum-timing design should be replaced by reliability-driven design for subthreshold Flip-Flops.
Size has minor effect on the performance while Vdd has large effect on performance due to its exponential character in current equation.

## Slide 15: References
Niklas Lotze, Maurits Ortmanns, Yiannos Manoli, “Variability of Flip-Flop Timing at Sub-Threshold Voltages”, International Symposium on Low Power Electronics and Design
Dejan Markovic, Borivoje Nikolic, Robert W. Brodersen, “Analysis and Design of Low-Energy Flip-Flop”, Low Power Electronics and Design, International Symposium on, 2001.
Vladimir Stojanovic, Vojin G. Oklabdzija, “Comparative Analysis of Master-Slave Latches and Flip-Flops for High-Performance and Low-Power Systems”, IEEE Journal of Solid-State Circuits, Vol. 34, NO.4
Alice Wang, Benton H. Calhoun, and Anantha P. Chandrakasan, “Subthreshold Design for Ultra-Low Power System.” Springer.
A. Wang and A. Chandrakasan, “Modeling and Sizing for Minimum Energy Operation in Subthreshold Circuit,” JSSC Vol 40 No 9 pp 1178-1786.